## Slide 1: IEEE1666 SystemC TLM2.0
Dipl.-Ing. Matthias Jung
Microelectronic Systems Design Research Group
Freitag, 12. Juni 2015
Coulpling gem5 with

## Slide 2: Virtual Prototypes In Industry
High-speed functional software models of physical hardware
Visibility and controllability over the entire system
Powerful debugging and analysis tools
Reuse of components for future projects
Fast Design space exploration (for HW engineers)
Easy to exchange, worldwide
Concurrent HW and SW development:
Effort
Time-to-Market
Hardware
development
Software
development
Testing /
Integration
Product support
and maintenance
Product support & maintenance
Earlier TTM
Higher Quality

## Slide 3: SystemC IEEE 1666
Modeling language for HW and SW components
Extends C++ to an event-driven simulation kernel
Different levels of accuracy
IEEE Standard, Maintained by Accellera
10-100x Faster than CA VHDL/Verilog Simulation
However, standard CA SystemC is not fast enough to boot, an operating system.

## Slide 4: Transaction Level Modeling
TLM
CA
SystemC
Pin Accurate
Simulate every event!!
100-10,000 X faster simulation!
CA
SystemC
TLM
Function Call
CLK
CLK
Source: Doulos Ldt. www.doulos.com

## Slide 5: Generic Payload
Initiator
(CPU)
Interconnect
(BUS)
Command
Address
Data
Byte Enables
Response Status
Extensions
Generic payload object
Payload reference
Initiator
Socket
Target
Socket
Initiator
Socket
Initiator
Socket
Target
Socket
Target
(MEM)
Target
(I/O)
&
Notes: SystemC:
  Erweiterung für C++
  Um HW und SW im Zusammenspiel zu simulieren
  IEEE Standard
  OSCI: Open SystemC Initiative
TLM2.0
  Transaction Level Modeling
  Erweiterung für SystemC um effektiv Kommunikation zu Simuliern
  Focus liegt hierbei auf der Funktionalität nicht auf der genauen Implementierung
  Transactions: Payload
    Command: read or write
    Adress: quell / zieladdresse
    Daten
  Nur eine Referenz wird übertragen  Simulation wird beschleunigt!
  Initiator: Master! prozessor
  Target: Slave! mempory

## Slide 6: TLM Coding Styles and Mechanisms
TLM Use Cases
TLM 2.0 Coding Style (Just Guidelines)
SW Application Development
SW Performance
Analysis
Architecture
Analysis
Hardware Verification
Loosely-timed
Single-phase, blocking API
Multi-phase, non-blocking API
Sockets
DMI
Quantum
Blocking transport
Generic
payload
Extensions
Phases
Non-blocking transport
TLM Mechanisms (Definitive API for enabling Interoperability)
Approximately -timed
Source: Doulos Ldt. www.doulos.com
Debug_transport, b_transport
nb_transport

## Slide 7: Tool Vendors for TLM2.0 VP
TLM is widely used in Industry:
The market of virtual platform tools:
Synopsys - Platform Architect
Cadence - Virtual System Platform
Mentor Graphics - Vista Virtual prototyping
Imperas – OpenVP
Virtual Platform Core Models:
ARM (Fastmodels):
  only LT models based on JIT, non-free
Carbon Design Systems:
  Cycle Accurate (CA) Models in TLM Wrapper, non-free
Imperas / OVP:
  only LT, Free
 An accurate, free available and changeable core model is needed

## Slide 8: Couple gem5 with SystemC
Since June 2014 gem5 supports a SystemC coupling. However, no TLM
Gem5 is build as a C++ library
It is hooked onto SystemC's event loop.
The hosting is achieved by replacing 'simulate' with a SystemC object, which implements an event loop using the SystemC scheduler mechanisms.
Currently only one gem5 instance can be in a SystemC simulation.
Events
Logic
Time
Events
Logic
Time

## Slide 9: Transaction Models in gem5
Timing
  The most detailed access: queuing delay + resource contention
  Similar to the TLM nb_transport interface.
Atomic
  Accesses are a faster than detailed access
  Used for fast forwarding and warming up caches
  Similar to the TLM b_transport interface
  Not good for performance simulation
Functional
  Similar to transport_debug
  e.g. loading binaries, avoiding deadlocks in multi-level cache coherent networks

## Slide 10: Coupling gem5 with SystemC-TLM
Gem5 World
TLM World
Transactor
(sc_port.{cc|hh})
GSPort::recvFunctional(PacketPtr packet)
port->transport_dbg(payload);
GSPort::recvAtomic(PacketPtr packet)
port->b_transport(payload, delay);
GSPort::recvTimingReq(PacketPtr packet)
port->nb_transport_fw(pl, ph, dly);
Transactor:
Gem5-Packet to TLM-Payload converter
Uses gem5 event queue as TLM-Payload-Event queue
Implements fully TLM2.0 compliant functionality

## Slide 11: Setting up an external Port in gem5
CPU
DRAM
UART PL011
...
X-Bar
ExternalPort
Python Config:

## Slide 12: Picking Ext. Port up in SystemC World
Instantiate gem5 as sc_module
Find external Port with sc_find_object
Instantiate a TLM target
Bind the target’s port with the external port of gem5

## Slide 13: Simple Traffic Generator Example

## Slide 14: Full System Linux Boot Example

## Slide 15: Results Slowdown
~3.5x
~16x

## Slide 16: Outlook
Use a TLM memory manager to be fully TLM compliant
Improve speed (e.g by implementing a TLM memory manager)
Fix some bugs regarding Atomic Access and Retry
Connect gem5 to DRAMSys (inhouse DRAM TLM Simulator)
Use gem5 in Synopsys Platform Architect
Currently on the gem5 review board:
#2753
http://reviews.gem5.org/r/2753/
Please test and give feedback